## Slide 1: Verification of rlgc2s() Function in Matlab
Davit Kharshiladze
Yifan Ding
Chulsoon Hwang

## Slide 2: Table of Contents
RLGC Matrixes
rlgc2s() Function Overview
Verification of the Function by Simple Transmission Line Simulation
Verification of the Function by Differential Pair of Stripline
Verification of the Function by IMLC Simulations

## Slide 3: RLGC Matrices
Diagonal elements [ describe self-resistance of each conductor and return path
Non-diagonal elements [ describe losses between conductors by effects such as proximity effect
Diagonal elements [ describe self-inductance (loop inductance) of each conductor
Non-diagonal elements [ describe magnetic coupling between different conductors (mutual inductance)
Diagonal elements [ describe dielectric leakage losses from a conductor and its return path
Non-diagonal elements [ describe dielectric leakage losses between different conductors
Diagonal elements [ describe capacitance of each conductor-return path pair
Non-diagonal elements [ describe electric coupling between different conductors
RLGC matrices fully describe behavior of transmission line groups. Giving large amounts of information, other important characteristics of the system can be derived from them.
In each matrix, conjugate indexed values are the same i.e.

## Slide 4: rlgc2s() Function in Matlab
rlgc2s() function allows conversion between distributed parameters to s-parameters of the system
( )
*order of ports are changed
For detailed information see this URL
R,L,G,C matrices can be 3 dimensional (NxNxM) where M is number of frequency points. This allows frequency dependent RLGC parameter conversion
S parameters are in Real Imaginary format
Example Snippet
Length of the transmission line
Per meter
distributed parameters

## Slide 5: Verification of the Function by Simple Transmission Line Simulation
Simple Model in Keysight ADS
Simulate simple circuit: Two-Ports connected by TL with frequency-independent RLGC parameters
Obtain S parameters from circuit simulator (In this case keysight ADS)
Create matlab script which converts same RLGC parameters to S parameters using rlgc2s()
Compare Obtained S parameters
To verify rlgc2s() function, series of tests were conducted. Simplest test was created using a single transmission line and two ports
Input Port
Output Port
Transmission Line (W-Element in ADS)
 | R | L | G | C
Values | 50 m | 1 nH/m | 0.01 S/m | 1 pF/m
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1m |  |  | 
Port Impedance | 50 |  |  | 
 | R | L | G | C
Values |  | 1 nH/m | 0.01 S/m | 1 pF/m
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1m |  |  | 
Port Impedance |  |  |  | 
Simple Matlab Script

## Slide 6: Verification of the Function by Simple Transmission Line Simulation - Results

## Slide 7: Verification of the Function by Differential Pair of Stripline
70 m
Second step in verifying was to use it in more complicated case. This time, RLGC parameters would be frequency-dependent
Create a differential pair of stripline in Ansys Q2D
Obtain distributed RLGC values for this configuration and S parameters
Feed RLGC values to rlgc2s() function to obtain S parameters using Matlab
Compare S parameters obtained from Matlab to S parameters obtained from Ansys Q2D
Positive Pair
Negative Pair
Ground
Ground
FR-4 Substrate
1.6mm
4mm
70 m
0.6mm
Matlab Script
Q2D Model
 | R | L | G | C
Values | Frequency Dependent |  |  | 
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1m |  |  | 
Port Impedance | 50 |  |  | 
 | R | L | G | C
Values | Frequency Dependent |  |  | 
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1m |  |  | 
Port Impedance |  |  |  | 

## Slide 8: Verification of the Function by Differential Pair of Stripline - Results

## Slide 9: Verification of the Function by Differential Pair of Stripline - Results

## Slide 10: Verification of the Function by Differential Pair of Stripline - Results

## Slide 11: Verification of the Function by Differential Pair of Stripline - Results

## Slide 12: Verification of the Function by IMLC Simulations
To further verify the function, we checked and compared IMLC simulation results to rlgc2s() converted results
Get RLGC and S parameter data from IMLC
Import RLGC parameters to Matlab
Use rlgc2s() to convert RLGC to S
Compare S parameters obtained from Matlab to S parameters obtained from IMLC Q2D
 | R | L | G | C
Values | Frequency Dependent |  |  | 
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1852.925 mil |  |  | 
Port Impedance | 50 |  |  | 
 | R | L | G | C
Values | Frequency Dependent |  |  | 
Frequency | 40 MHz – 60 GHz (40MHz Step) |  |  | 
Length | 1852.925 mil |  |  | 
Port Impedance |  |  |  | 

## Slide 13: Verification of the Function by IMLC Simulations - Results

## Slide 14: Verification of the Function by IMLC Simulations - Results